## Slide 1: ILC
Flavor Physics Workshop 2021, 30 Sept. 2021
Masao KURIKI
Graduate School of advanced science and technology, Hiroshima U.
Accelerator Technology

## Slide 2: Contents
1
ACCELERATOR EVOLUTION
2
LINEAR COLLIDER DESIGN COCEPT
3
ILC ACCELERATOR TECHNOLOGY
4
SUMMARY

## Slide 3: ACCELERATOR EVOLUTION

## Slide 4: J. J. Thomson
2008 LHC starts at CERN
110 years
Length x 140000
Energy x 70,000,000
1897 Discovery of electron by crookes tube.
Length 20 cm
Energy 100 keV
Circ. 27 km
Energy 7 x 7TeV
The first contact to elementary particles

## Slide 5: ACCELERATOR PERFORMANCE
EVENT RATE
GIVING A LARGE NUMBER OF EVENTS FOR GOOD STATISTICS
REACH
ABILITY TO PRODUCE HEAVY PARTICLES FOR NEW PHYSICS
ACCURACY
DEFIEN INITIAL STATE ACCURATELY FOR THE FULL EVENT RECONSTRUCTION.
LUMINOSITY
CME
KINEMATICS

## Slide 6: DC Accelerator : Cockcroft-Walton
Acceleration by static field.
Acceleration voltage is limited by discharge.
Acceleration is only once.
The highest energy is limited by vacuum discharge.

## Slide 7: AC（RF） Accelerator
Acceleration by temporary varying field.
Acceleration can be repeatable.
The energy is unlimited principally.
This is dawn of HIGH ENERGY ACCELERATOR.
G. Ising
R. Wideroe
L. Alvarez

## Slide 8: Power of Collider
Don’t move !
Fixed target
Collider
If the particles move after collision, less effective.
125GeV + 125 GeV
（250GeV ILC ）
62,500,000 GeV
（ 250,000 ILC ）
Beam energy for Higgs
(e+e- -> Zh)

## Slide 9: Energy Frontier
HERA
PETRA
DORIS
LEPLHC
SppS
ISR
TRISTANKEKB
SLC
PEP
SPEAR
SSC
TEVATRON
EUROPE
ASIA
US
International Linear Collider
Many Ring Colliders, but only one Linear collider
Why we built linear colliders?
Notes: TRISTAN 3km; LEP 27km; SppS 6.9km; ISR 0.942km; HERA 6.336km; PETRA 2.3km; DORIS 0.3km; SLC (linac) 3.2km; PEP 2.199km; SPEAR 0.234km; TEVATRON 6.3km; SSC 87.1km; ILC 50km (1 TeV)

## Slide 10: Power Consumption
Dawn of New epoch
Linear Collider
1. Beam is accelerated and damped.
2. Power is also linear to the beam power.
Ring Collider
1. Beam is circulating.
2. Lost beam is provided by injector.
3. Additional power by SR.

## Slide 11: Energy evolution of accelerator
Obstacle and breakthrough
DC accelerator
RF accelerator + Fixed Target
Ring Collider
Linear Collider
20MeV
200GeV*
600MeV
(*)the number is for e+e- collider.
Invention of
RF accelerator
Invention of
Collider
Invention of
Linear Collider

## Slide 12: Linear Collider Design Concept
Linear Collider character is quite different from that of ring colliders.

## Slide 13: Pros and Cons of linear collider
Pros
No energy loss by synchrotron radiation.
The beam can be polarized.
Strong against the beam-beam effect, because we don’t care about the beam after collision.
Cons
The beam power can’t be high, otherwise the electricity could be huge.
Need a high gradient, otherwise the length could be humongous.

## Slide 14: Luminosity Gain for LC
A high luminosity with a limited beam power is a key of LC.
Suppress for saving electricity
Minimize for larger luminosity.
Ring Collider
Linear Collider

## Slide 15: Beamstrahlung
Synchrotron radiation with magnetic field generated by the collision partner.
It causes the energy tail of the beam resulting a worse energy resolution.
Ampere’s law

## Slide 16: Luminosity Gain for LC
A high luminosity with a limited beam power is a key of LC.
To keep BS, only sy is minimized.
Minimize for large luminosity
To keep BS, it should not be too small.
Ring Collider
Linear Collider
Solar car
Suppress for saving electricity
Collider with a limited beam power = E-Collider

## Slide 17: Beam Focusing (Hour glass effect)
: Beam focusing depth at IP.
: Bunch length.
Focusing Depth
If , the luminosity is small, because only a fraction of beam is focused.
If , the luminosity is large.
sz＜by,
  No large enhancement for luminosity
  Enhance Beamstrahlung
sz＝by is the optimum.

## Slide 18: Luminosity Scaling
Beam power and electricity：
Beam size at IP: Energy spread by BS :
Normalized Luminosity
Luminosity

## Slide 19: Luminosity Scaling
Normalized Luminosity
Experimental Design
Physics
System
Optimization
Accelerator

## Slide 20: ILC Accelerator Technology

## Slide 21
ILC Functions
3. Superconducting Accelerator
1. (Polarized) Electron and Positron
2. Radiation Damping
4. Final Focus

## Slide 22: GaAs photocathode
GaAs crystal for polarized electron generation.
By breaking the degeneration of the valence band, spin of excited electron depends on the helicity of photon (circular polarization).
Degeneration is broken by strained super-lattice crystal giving 90% polarization.

## Slide 23: ILC Positron Source
Two concepts of positron source : Electron Driven (conventional) and Undulator.
E-Driven : Brems+pair-creation. Technically established, but unpolarized.
Undulator : Gamma from undulator radiation driven by >100 GeV driver. Technically new, but polarization is useful for physics.

## Slide 24: Positron Capture
Positron capture is a key issue for both scheme.
  Matching device
  RF capture
  Energy Compressor
RF capture
Booster
ECS

## Slide 25: Flux Concentrator as AMD
Flux Concentrator (pulse magnet) generates AMD field.
AMD (Adiabatic Matching Device) field
Adiabatic invariance on the cyclotron motion
Since Bi>B(z), is suppressed by AMD.
  170 mm
16mm
100mm
target

## Slide 26: RF capture
Generated positron is widely distributed in energy and .
Positron is decelerated initially. Due to the large , positron cause phase slip.
Positron is moved to acceleration phase by the phase slip.
Acceleration suppress the phase slip. The positron is swept up at the phase.

## Slide 27: Damping Ring
Cool down the beam
1. Beam loose their energy by SR.
2. The energy is recovered by re-acceleration .
3. SR decreases the momentum in x, y, and z, but cavity provide only pz. The beam is aligned and cooled.
Radiation
Damping

## Slide 28: Superconducting Accelerator
SC Cavity
Thermal shields
(80K, 5K)
Liq. He
Gas He
return
Cryomodule
(8 or 9 cavities)
Super-coducting Cavity

## Slide 29: SC cavity performance
40.9 MV/m
RF power limit
ILC spec.
E=35MV/m
Q=0.8 x 1010
Thermal Quench
Field emission

## Slide 30: Pathology
Thermal Quench
Defects on the equator cause thermal quench because the large current.
It can be detected by temperature mapping.
Field emission
Defects on the iris causes field emission.
It leads Q-slope by the energy loss.
It can be detected by X-ray mapping.
equator
iris

## Slide 31: Summary STF Phase-II
All cavities satisfy the ILC specification: 35 MV/m± 20%.
Average gradient is 36.8 MV/m.
The highest is 41 MV/m which is a national record in 2013.
The field is limited by the available power (not quench).
The cavity fabrication yield (ratio of good cavity) is more than 90%.
Ready for fabrication.

## Slide 32: Final Focus
To improve luminosity, the beam should be focused down to 5.7nm in transverse direction.
A strong focusing is not enough. Controlling chromaticity is a key issue.
Chromaticity : Aberration by energy spread.
Chromatic aberration is corrected by achromatic lens (Sextupole + Quadrupole).
High
energy
Low
energy

## Slide 33: Local Chromaticity Correction
Chromaticity by Q is corrected by sextupole with dispersion locally.
Sextupole generates non-linearity. Two pair of the lattice cancels their non-linearity to each other.
The same beam line but with lower energy has been examined at ATF2.
Bending
Sext. Quad.
Sext. Quad.
IP
Sext. Quad.
Sext. Quad.

## Slide 34: Final Focus Test at ATF2
ILC FF Beam line is simulated at ATF2 experimentally.
Beam size is measured with Laser fringe monitor (AKA Shintake monitor).
41 nm beam size was confirmed. It should be compared with 37nm at ILC.

## Slide 35: Traveling Focus option
By considering hour glass effect, is not effective to obtain a large luminosity.
If we place “a lens” at IP, the beam size can be kept small.
We use the beam as the lens because the beam attracts to each other by Coulomb force.
The focal point should be moved along the bunch: traveling focus.
Traveling focus is possible with crab. Cavity + sextupole.
It is possible, but sensitive to field error, etc. That is why it is an option.

## Slide 36: Summary
1. New Epoch
Linear collider is a new epoch on the high energy accelerator to extend our reach since the invention of collider.
2. LC is an E-collider
LC concept is realizing a large luminosity with a limited beam current.
3．LC Technology
High gradient linear accelerator and nano-beam is key technologies of LC.
4. ILC Accelerator is ready
Accelerator technology to construct ILC is ready.