## Slide 1
Masao KURIKI
Graduate School of Advanced Sciences of Matter,
Hiroshima University
大阪市立大学
粒子物理学特別講義Ⅱ
加速器設計の原理と構成要素
3. Injector and Particle source
ALLPPT.com _ Free PowerPoint Templates, Diagrams and Charts

## Slide 2: Contents
Injector,
Electron Source,
Positron Source,
Ion Source,
Summary

## Slide 3
Injector

## Slide 4: Injector
What is the injector?
  Generate accelerate-able particle beams;
What is the accelerate-able beams?
  Right amount : Charge
  Right shape : Beam size, emittance, bunch length
  Right direction: along beam line
  Right time : timing, phase
Injector
Accelerator
Transport line
IP

## Slide 5: Electron Gun
Generate electron beam
  Right amount : Charge
  Right shape : Beam size, emittance, bunch length
  Right direction: beam line
  Right time : timing, phase
3.2nC
Extraction Field
Cathode
Beam

## Slide 6: Bunching
Bunching : Bunch the beam. What is the bunch?
  Beam : collimated particle flow.
  Bunch : collimated and clustered particle flow. The length should be short enough comparing to the RF period for uniform acceleration.
Beam
Bunch

## Slide 7: Bunching (2)
Bunching: Shorten the longitudinal length of the beam.
    Right amount : Charge
    Right shape : Beam size, emittance,bunch length
    Right direction: beam line
    Right time : timing, phase
3.2nC
Bunching

## Slide 8: Injector Concepts
3.2nC
To Acc.
Thermionic Cathode
Photo-cathode
Field emitter
Extraction Field
CW Beam
Long bunch beam
Short bunch beam
DC field
RF field
Cathode
Bunching
Pre-buncher
Sub Harmonic Buncher
Buncher

## Slide 9: Bunch Compression

## Slide 10: Bunch Compression
In any RF accelerators, the beam should be concentrated in a short period of longitudinal space for small energy spread;
  E=E0cos(ωt-ks), kds«1 for efficient acceleration.
Bunch compressor(buncher) shorten the bunch length down to an adequate size for acceleration.

## Slide 11: Bunch Compression (2)
There are two ways for bunch compression:
  Velocity Bunching
  Magnetic Bunching
Velocity bunching is effective only for low energy;
  Some particle source can generate only long bunch or continuous beam.
  It should be bunched for RF acceleration.
Magnetic bunching is effective for all energy region.
  It is employed sometimes to get extremely short buhc after acceleration.
  It is also used to compensate the bunch lengthning in DR for Linear colliders.

## Slide 12: Velocity Bunching
Bunch compression is performed by velocity modulation within a bunch;
  Bunch head is decelerated.
  Bunch tail is accelerated.
Velocity is modulated by energy modulation according to
Velocity is saturated to c at γ>>1. Then, it works only for low energy particle (β<1).

## Slide 13
Energy modulation by RF cavity,
In linear approximation,
Next higher order

## Slide 14
Time for drift is
With the energy modulation,
Energy modulation for particle with dt from bunch center,
If dt+dt=0, the particles are gathered at the center,
dt
dt
t
dE/E

## Slide 15: Magnetic Bunching
Energy Modulation : RF cavity.
Dispersive section : different path for different energy.
Bunch head (tail) travels longer (shorter) path and bunch length becomes shorter.
By E.S. Kim

## Slide 16
Bunch compression is performed by energy modulation with a momentum compaction.
  Chicane, Wiggler, Arc, etc.
A path length difference with a momentum compaction, ∆z is
It works well for any energy particle.

## Slide 17: Matrix Formalism
Acceleration
Deceleration
Drift
δ(ΔE/E)
z
Bunching can be formalized with transfer matrix in linear approximation.
Energy modulation is made by RF (acc- and deceleration).
Drift space (velocity bunching) or momentum compaction (magnetic bunching) rotates the beam in phase space with 90 deg.

## Slide 18: R-matrices
Beam transfer in longitudinal phase space,
Drift space
,
Dispersion section
RF Energy modulation
,

## Slide 19
δ(ΔE/E)
z
Transfer of BC section is given as
With bunching condition
Velocity bunching:
Magnetic bunching:
R65
R56

## Slide 20
δ(ΔE/E)
z
R65
R56
When the bunching condition is satisfied,
The position z2 does not depends on z1. The bunch center is determined by RF phase (zero cross).
In general, RF signal is a better reference to determine timing. It is suitable for stable operation.

## Slide 21
δ(ΔE/E)
z
Final bunch length after an optimized BC section is determined by the initial energy spread;
The actual bunch length is also limited by non-linearity as

## Slide 22: Energy Compression
Energy compression is a reverse process of the bunch compression as,
The final energy spread is
δ(ΔE/E)
z
R65
R56

## Slide 23
Particle Source

## Slide 24: Why is the particle source important?
Materials
Chef
Food
Particle Source
Accelerator
Experiment

## Slide 25: Electron Source

## Slide 26: Fundamental Process
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Thermal emission
Field emission
Thermal emission
Photo-electron emission
Electric field
laser
[e-
Secondary electron emissio

## Slide 27: Electronic States
e-
e-
e-
e-
Electrons are confined in a well potential.
At T=0, electrons are in ground states.
At T>0, some electrons are excited by thermal energy.
Vacuum
(free space)
Well potential
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e
-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 28: Electronic States
Electrons are distributed according to Fermi-Dirac Distribution.
Fermi energy : the maximum electron energy state at T=0.
Work-function : height of the vacuum cliff from the Fermi energy.

## Slide 29
Vacuum state
Fermi Level
Electrons in grond states
Peaceful Cliff

## Slide 30
Fermi Level
Hot Electrons
Some extreme guys are extracted as beam
Once they are excited....

## Slide 31: Thermal Electron Emission
If the temperature is sufficiently high, so that electrons are distributed up to more than the vacuum level (E0), the electrons escape out to the outside.
The gap between the vacuum level and the Fermi energy is Work function, φ, which characterize the thermal emission.

## Slide 32: Emission Density
Number of emitted electron:
In depth (z-direction)
Kinetic energy for z-direction must be more than vacuum potential energy, μ+Φ
Number of electron emitted from the cathode is given by

## Slide 33: Richardson-Dushman Equation
T: Temperature (K)
k : Boltzmann constant (J/K)
e : electronic charge(C)
m : electron mass(kg)
h : Plank constant (Js)

## Slide 34: Field Emission (1)
FE is electron emission observed when a high electric field is applied.
  Large surface field makes the potential barrier very thin.
  The tunnel current becomes significant with >1E+8 V/m.

## Slide 35: Field Emission (2)
Electron
density
Tunneling
probability
WKB method
Fowler Nordheim Formula

## Slide 36: Fowler-Nordheim Plot
k: local field enhancement by surface condition,
Taking ln(J/F2) and plotting as a function of 1/F,
The gradient gives information on the surface condition, k.
Fowler-Nordheim formula with field enhancement factor κ
ln(J/F2)
1/F

## Slide 37: Photo-electron Emission
Photons excite electrons into higher energy states.
If the states are higher than the vacuum level, the electrons goes to vacuum.

## Slide 38: Fowler Equation
Fowler equation gives photo-current spectrum.
Still some current in δ<0 due to the thermal energy.
δ=h(ν-ν0)/kT

## Slide 39: Quantum Efficiency
Quantum Efficiency, η, is practically used to quantify the photo-electron emission

## Slide 40: Polarized electron
Polarized Electron is generated by photo-emission with GaAs semiconductor cathode.
For polarization, the direct transition is essential.
Transition from the valence band (VB) to conduction band (CB) by circularly polarized photon is spin dependent.
VB
CB

## Slide 41: Excitation
Transition probability ~ Fermi's golden rule
  M: Matrix element
  D: joint density of states of ħω photon
  f: Fermi distribution function
Considering only near of the band gap, the transition probability is proportional to M2.

## Slide 42: Matrix Element of GaAs
Band gap of GaAs is Γ point ( k=0).
  Valence Band:
    J=|3/2,±3/2> (heavy hole)
    J=|3/2, ±1/2> (light hole).
  Conduction Band:
    J=|1/2,±1/2>
Matrix Element of transition (Clebsh-Gordon coef.）
  Heavy hole: /2
  Light hole: 1/2
Conduction
band
Valence
band

## Slide 43: Polarization
By energy and helicity limitation, only two of six transitions are possible.
Number of excited electron are polarized by 3:1 matrix amplitude.
Right handed polarization
Left handed polarization

## Slide 44: High Polarization from SL GaAs
Super-lattice structure breaks the degeneration.
The polarization is enhanced by suppression.
92% polarization, 1.6% QE
Strain relaxed
super-lattice
24 layer
Buffer layer
Base plate

## Slide 45: Photo-Electron Emission from a direct band-gap Semiconductor
Transition probability
State of Density

## Slide 46
Dispersion relation of conduction band
Dispersion relation of valence band)
Dispersion relation of transition

## Slide 47
Combined State of Density
Energy in the conduction band
Escape probability of electrons in CB
Quantum Efficiency

## Slide 48: Space Charge Limit
Electron terminates the electric flux (Gauss's law).
Electric field is weakened by the space charge.
When all flux is terminated by the charge, the field at the cathode surface is disappeared (no further emission).

## Slide 49: Space Charge Limit (2)
Poisson equation is
The current density J is given by the charge density ρ and velocity v ,
According energy conservation,
Cathode
(z=0, V=0)
Anode
(z=d, V=VA)
z
Charge density r(z)

## Slide 50: Child-Langmuir Law
V and d : voltage and distance between two electrodes.
S : cathode area
P : perveance defined as;

## Slide 51: DC Gun (Pierce Type Gun)
Solution for SC limited flow;
z
y
V=0 equi-potential line:
By setting an electrode (Wehnelt) with this angle, SCL flow is produced.

## Slide 52: Thermionic DC Gun Pierce Type Gun
Wehnelt electrode
Anode electrode
Thermionic
Cathode
Electron Beam

## Slide 53: Photo-Cathode DC Gun
Photo-electron emission for beam generation.
Beam extraction by DC field.
The bunch structure (repetition and duration) is determined by the laser.
Beam energy is determined by DC voltage.
-V
Cathode
Anode
Beam
Ceramic
HV terminal

## Slide 54: RF Gun (1)
Electron is generated in inside of RF cavity.
RF field for beam extraction.
Laser photo-cathode type is popular.
Beam from thermionic cathode type has a wide energy spread.

## Slide 55: RF Gun(2)
Typical cavity configuration is N+0.5 cells.
TM01, pi-mode.
Energy at the gun exit is given by
P : RF input power,
R :shunt impedance
Typical field is 10-100 MV/m resulting several MeV energy.

## Slide 56
Beam Emittance from Cathode

## Slide 57: Beam Emittance
Emittance is defined as area in the phase space where particles occupy. The phase space is defined x and x'=dx/ds
In general, RMS emittance is given as
If there is no correlation between x and x',
ps
px
p

## Slide 58: Normalized emittance
p2
In acceleration, transverse momentum px is conserved, but the total momentum p is increased as
The emittance is inversely scaled. To avoid the energy dependence (γβ) on the emittance, the normalized emittance is defined
ps
px
p1

## Slide 59: What is matter?
Emittance shows the quality of the beam.
Small emittance beam can be focused down to a small spot size.
Small emittance beam can be extremely parallel.
The shape of the beam depends on the optics, but the emittance is invariant in the frame of linear optics.
Linear
Optics

## Slide 60: What is the fundamental limit on the emittance?
Everybody wants small emittance beam, but what is the limit?
One of the limit is the intrinsic emittance which the emitted beam from the cathode already has.
The source of the intrinsic emittance of cathode is thermal energy and laser energy (photo-cathode case).

## Slide 61: Emittance of Beam from Thermionic Cathode (1)
Thermionic electron emission density
Total transverse energy
The average transverse energy per electron is

## Slide 62: Emittance of Beam from Thermionic Cathode (2)
Thermal energy is,
The transverse emittance is

## Slide 63: Emittance of Beam from Photo-cathode (1)
Transverse energy from photo-emission is
with T=0 approximation,

## Slide 64
The average transverse energy
The average momentum,
Emittance is

## Slide 65
Accounting thermal energy, the transverse energy becomes
The transverse emittance is

## Slide 66: Space Charge Force
非線形な空間電荷効果はビームサイズ（横方向、進行方向）の増大、 エミッタンス増大、チューンシフト、などの様々な悪影響を与える。
この影響を低減するには、二つの方法がある。
  空間電荷効果を線形化する。
  空間電荷効果そのものを低減する。

## Slide 67
空間電荷効果の線形化は、電荷密度を均一化することにより実現できる。半径aの均一な円筒に単位長さ当たりN個の電子があるとすると、
ローレンツ力は
確かに線形化されており、1/g2に比例するので、加速により低減する。

## Slide 68: Positron Source

## Slide 69: Positron Production
There is only few positrons in nature.
Two ways to produce positrons :
  Create radio-active elements, which β+ decays; p → n e+ ν.
  Pair-creation ; γ → e+ e-
All of the positron beam sources with a time structure, employ the pair-creation process.

## Slide 70: Positron Production (2)
Photon interaction in material:
  Photo-electron effect(<1MeV)
  Compton scattering (1-10MeV)
  Pair-creation (>10MeV)
Gamma ray, energy >10MeV is required for effective pair creation.
σp.e. : photo-electron
σCompton:Compton scattering
κnuc, κe: pair creation
(from Particle Data Group, http://pdg.lbl.gov)

## Slide 71: Need Photon?
We need photons in gamma ray region to create positrons through the pair creation.
How to create the photons?
  Brems-strahlung: electron interaction in material. Very effective.
  Undulator radiation: Synchrotron Radiation. Need very long undulator with very high energy electron.
  Inverse Compton scattering : Laser and electron interaction. Need very high density laser field.

## Slide 72: Electron Driven
Electron is decelerated by nucleus field.
Photon is emitted by the energy conservation.
Gamma rays are obtained with MeV or GeV electrons.
The gamma rays are converted to positron and electron pair by Pair-creation process.
-
-
+
+
-
+

## Slide 73: Electron Driven(2) Bremsstrahlung
Bremsstrahlung is dominant in high energy region.
Below some Ec, ionization is dominant.
When high energy electrons are injected into material, electrons loose their energy by Brems-strahlung.
When the energy becomes less than Ec, Brems-strahlung is not dominant.
Critical Energy Ec

## Slide 74: Cascade Shower
Radiation length X0:
Energy at each steps:
This process is continued up to;
n=0
n=1
n=2
n=3
n=1
n=4

## Slide 75: Cascade Shower (2)
As consequence of the cascade shower by the high energy electron in material, many positrons are generated.
Number of positron is maximized at shower max determined by X0, E0, and Ec.
Courtesy of T.Kamitani

## Slide 76: Direct Pair Creation
10s MeV photons directly generate positrons through the pair creation process.
Due to this simplicity, if the photons are polarized, the positrons are also polarized. (Polarized Positron).
# of particles is not multiplied. Each photon can generate only up to one positron. We need many photons.

## Slide 77: Undulator Radiation (1)
In alternate dipole B field(undulator), electron wiggles periodically.
Electron speed along the longitudinal axis is less than speed of light due to the orbit.
Photons are emitted to the direction where wave-plane distance corresponds to integer of the photon wave length.
B+
B-
B+

## Slide 78: Undulator radiation (2)
To obtain >10MeV gamma ray, more than 100 GeV drive beam is required.

## Slide 79: Laser Compton(1)
Inverse Compton scattering between laser photon and electron beam.
Laser photon (wavelength is in μm order) is scattered by high energy electron and its energy is boosted.
As a result, high energy gamma-ray is obtained.
EL : Laser energy 1.2eV @ 1μm.
Electron beam 1GeV, γ=2000.
Eγ ~ 16MeV

## Slide 80: Laser Compton (2)
Laser acts as a quite short period undulator. The energy from Compton scattering is rewritten as
where λL is laser wave length.
High energy gamma (several 10s MeV) is obtained with few GeV electron beam.
Laser focal length is limited to Rayleigh length. It is difficult to make a long “laser undulator”.

## Slide 81: Polarized Positron
T.Kamitani
Energy, angle, and helicity of photon from undulator and Laser-Compton are correlated.
By taking gammas in super-forward direction, gamma rays and positrons are polarized.

## Slide 82
Positron Capture Optics

## Slide 83: Positron Capture
The generated positrons are distributed in a small spot size and in a large momentum space. To convert it to the parallel beam, a couple of solenoid-like magnetic field with different profile are employed.
  QWT (Quarter Wave Transformer)
  AMD (Adiabatic Matching Device)

## Slide 84: QWT
QWT consists from initial strong solenoid field , Bi, and weak solenoid field, Bf, along z direction.
Accelerator is placed in Bf region for adiabatic damping.
It transforms 90o in the phase space, that is why it is called as Quarter Wave Transformer.
pt
r

## Slide 85
Positrons are circulated with radius ρ
Time to travel πρ in xy plane,
Time to travels Li
If t1=tL,

## Slide 86
Magnetic flux in circle with 2r radius at Bi and Bf region are
Because no magnetic monopole, there is transverse magnetic flux at the boundary. Taking the integral of Bt(z) along z,

## Slide 87
Momentum kick by Bt is
Integrating this equation, the total kick is
pt after the kick is

## Slide 88
Pt(t) after the kick is
Radius of the circulating motion does not change,

## Slide 89
Initial strong solenoid magnet with bucking to cancel B field on target.
Bf is 0.5 T.
NC L-band accelerator is placed in Bf region.

## Slide 90: AMD
AMD consists from the initial strong solenoid field which decreases continuously.
Acceleration for the adiabatic damping.

## Slide 91
In xy plane, positrons are circulated with radius ρ(z),
If parameters of the motion is changed slowly compare to the circulating frequency, adiabatic invariant is constant during the motion.

## Slide 92
Due to the adiabatic condition,
The radius is

## Slide 93
Transverse momentum and orbit radius at AMD exit is
Twice of the radius has to be less than accelerator aperture a,
For adiabatic condition,

## Slide 94: AMD example
AMD field is produced by flux-concentrator.
Primary coil induces eddy current in the inner conductor.
Because of the tapered shape of the inner conductor, the magnetic field is concentrated.

## Slide 95
Positron Source Concepts

## Slide 96: Positron Source
Positron source is a system, composed from:
  Drive Beam (Electron or Photon)
  Conversion target
  Matching Device
  Capture Accelerator
Three concepts:
  Electron driven (conventional), Undualtor, and Laser Compton.

## Slide 97: Electron Driven
Sub or Several GeVs driver electron beam.
High Density Material for shower development.
Positron capture by Solenoid, QWT, or AMD.
NC accelerator tube with solenoid focusing.
All positron sources based on accelerator every built, is this concept. That is why it is called as “conventional”.

## Slide 98: Undulator Positron Source
More than 100 GeV electrons as driver for > 10 MeV gamma rays.
With helical undulator, polarized positron is generated.
Pulse by pulse spin flipping is difficult.

## Slide 99: Compton Positron Source
Compton back scattering with several GeVs electron generates ~ 30 MeV gamma rays.
Positron polarization with circularly polarized laser.
Pulse-by-pulse polarization flipping is possible.

## Slide 100: Ion Source

## Slide 101: Ion state
Energy State of Hydrogen
Hydrogen atom H0
Negative ion H-
Positive ion H+
Ionization energy 13.6 eV
Electron Affinity 0.75 eV
H- is the most stable state. No extra energy is required to generate H-.
Ionization energy to create H+ is more than 10 eV.
H- and H+ are generated with different ways.

## Slide 102: Ionization energy and electron affinity
Atom | 1st Ionization Energy(eV) | Electron Affinity (eV)
H | 13.6 | 0.75
He | 24.5 | <0
Li | 5.4 | 0.62
C | 11.3 | 1.27
N | 14.5 | <0
O | 13.5 | 1.46
F | 17.4 | 3.4
Ne | 21.5 | <0
Na | 5.1 | 0.55

## Slide 103: Positive ion generation
Cross section
Electron energy
H+ can be generated by electron impact with energy more than the ionization energy.
To maximized the yield, electron energy should be adjusted at the peak of the cross section.
10 100 1000 (eV)

## Slide 104: PIG Ion Source

## Slide 105: ECR Ion Source
B

## Slide 106: Negative Ion Source
Because the negative ion is stable, impact energy is not necessary.
To maximized the yield, electron intensity should be maximized.
  Charge exchange production.
  Volume production.
  Surface production.

## Slide 107: Charge Exchange Production
H- ion
Gas
or
Thin foil
H+ ion

## Slide 108: Volume production
Disassociation of vibrational
excited molecule.

## Slide 109: Surface Production Source
Due to the potential bend by mirror charge effect, the potential in near of the metal surface is lowered.
Free electron is transferred to atom through the tunneling effect.

## Slide 110: Cesiation
By adsorbing Cs on metal surface, the work function can be lowered to 1.1 eV.
The yield can be enhanced by this treatment.

## Slide 111: H- Ion Source

## Slide 112: Summary
Principle of particle generation for electron, positron, and ion are briefly explained.
Particle source determines the total performance of the accelerator.
Electron is generated by thermionic, photon-electron, and field emission.
Positron is generated by pair-creation.
Positive and negative ions are generated with different principles.
Injector is a subsystem forming the accelerate-able beam.