## Slide 1
Masao KURIKI
Graduate School of Advanced Sciences of Matter,
Hiroshima University
(material is taken from Lecture by T. Tanaka, Sp8)
ALLPPT.com _ Free PowerPoint Templates, Diagrams and Charts
Foundation of FELs
(Slides made by T. Tanaka)

## Slide 2
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 3
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 4: Synchrotron Radiation & Laser
Laser
Photon Science
first observed in 1947
radiation by a relativistic electron beam
work as laser-like sources, where conventional lasers are not available
first realized in 1960
fully coherent source by stimulated emission
applicable in spectral regions where reflective mirrors are available
SR

## Slide 5: No Practical Lasers in X-ray Region
until recently
Lasers and their wavelengths currently available
SR has been a good alternative to “X-ray” lasers!

## Slide 6: SR & Various Sources
SR provides much higher brilliance in x-ray regions.

## Slide 7: However,……
Four parameters to characterize the laser source performance
  Temporal & Spatial coherence, Brilliance, Bose degeneracy
Item | Laser (800nm) | SR (0.1nm)
Temp. Coherence | ~100% | ~10-5%
Spat. Coherence | ~100% | ~0.1%
Peak Brilliance | ~1028 | ~1023
Bose Degeneracy* | 1013 | ~10-4
*Number of photons (=Boson) occupying a single mode (state)
Source performances of SR are far from the laser source!

## Slide 8: What We Learn in This Lecture?
Free Electron Laser (FEL) as an advanced form of SR sources
How FEL Works?
  Coherent radiation
  Microbunching
  Characteristics of FEL radiation
  Numerical examples
ERL: another direction of SR sources evolution

## Slide 9
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
Characteristics of FEL radiation
ERL: what’s it?

## Slide 10: Spontaneous & Coherent Radiation (1)
In general, 109-1010 electrons are contained in an electron beam (bunch)
Radiation processes are classified according to how photons accumulate
  Spontaneous：random accumulation
  Coherent：in-phase accumulation
Which is more dominant depends on the electron bunch length () relative to the wavelength of radiation (l)

## Slide 11: Spontaneous & Coherent Radiation (2)
l
Spontaneous
Coherent

## Slide 12: Spontaneous & Coherent Radiation (3)
Spontaneous Radiation
  Bunch Length > Wavelength
  Summation as photons: # photons enhanced by N (=# electrons)
Coherent Radiation
  Bunch Length < Wavelength
  Summation as waves: amplitude enhanced by N
  # photons (∝|amplitude|2) by N2
Intensity of coherent radiation is N (=109~1010) times the spontaneous.

## Slide 13: Example of Coherent Radiation
E=8GeV
B=1T
Dt=100fs
l=30mm

## Slide 14: Coherent Radiation by Microbunches
Coherent at the wavelength of l
FEL is coherent radiation emitted by an electron beam with microbunches
l
Microbunch
l

## Slide 15: General Layout of FELs
Highly-brilliant Electron Beam
FEL
Pulse
Injector
Bunch
Compressor
Main
Accelerator
Undulator
FEL amplification takes place here!

## Slide 16
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 17: Basic Concept of FELs
Electron Beam
Microbunches
Amplified Light
Undulator
Seed Light
What’s the laser medium in FELs?
Free electrons?
Free electrons moving in the undulator field!
z
x

## Slide 18: Electron Trajectory in an Undulator
E=8GeV,K=1,lu=5cm：bxmax=64mrad, xmax=0.5mm
Undulator field with period lu
Transverse
Velocity
Trajectory
K Value
Deflection Parameter

## Slide 19: Velocity Modulations
Original value
transverse velocity
longitudinal velocity
Average Value
Oscillating Term
Undulator magnetic field induces:
  Horizontal (x) oscillation
  Longitudinal (z) oscillation
  Effective deceleration ()

## Slide 20: Slippage
Because of the velocity difference ( and ), photons overtake electrons while they travel the undulator: Slippage Effect
z
x
: slippage length over lu
= fundamental wavelength l1
e-
photon

## Slide 21: What’s Fundamental Wavelength?
z
x
Radiation with l1 is in phase with e-
  Intense spont. radiation at l1
  Continuous interaction between radiation and e- (next slide)

## Slide 22: Interaction with Radiation
Continuous interaction with radiation
Dg > 0 in (ii), (iv,…)
Dg < 0 in (i), (iii), (v,…)
Periodic energy modulation with l1

## Slide 23: Longitudinal Dispersion
z
x
e-(g)
e-(g’<g)
Lower-energy electrons are left behind the higher-energy ones

## Slide 24: Mechanism of Microbunch Formation
Sinusoidal Magnetic Field
Effective Deceleration
Slippage
Horizontal Oscillation
Continuous Interaction
Longitudinal Dispersion
Energy Modulation
Density Modulation
(Microbunch)
Radiation with l1

## Slide 25: Microbunch Formation in Phase Space
Interaction with Radiation
Longitudinal Dispersion
l1

## Slide 26: FEL Amplification
Microbunching
Coherent Radiation
Coherent Radiation
FEL Amplification =
Positive Feedback Loop of
Microbunching through interaction with radiation
Intensify radiation by coherent radiation
Microbunching

## Slide 27
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 28: FEL Equation
FEL Equation
To describe the FEL amplification, we need to consider:
  Electron dynamics in 6D phase space
  Interaction between e- and radiation
  Amplification by coherent radiation
  Diffraction of radiation
Rigorous solution needed For quantitative estimation
For qualitative understanding, simplified form with some approx. is enough!

## Slide 29: 1-D & SS Approximation
1-Dimensional and Steady State Approximation:
Initial distribution functions (at z=0) do not depend on x,y,t
Radiation amplitude and microbunch grows as z, but does not depend on x,y,t
amplitude
of radiation
microbunching
constant
current

## Slide 30: FEL Equation under 1D & SS
Under 1D & SS approximations, the FEL amplification is described by normalized variables as a function of normalized coordinate as follows:
Complex amplitude of radiation
Energy and position of j-th electron, relative to a reference electron
Longitudinal dispersion
Energy variation by interaction with radiation
Growth of radiation by coherent radiation

## Slide 31: Solving the 1D FEL Eq. (Analytical)
(2)
(3)
(2)
(1)’
uniform distribution
small energy deviation
0
Radiation growth equation under 1D & SS

## Slide 32: Solving the 1D FEL Eq. (cont.)
Simple propagation
Decaying field
Growing field
For large , only the growing field survives

## Slide 33: Solving the 1D FEL Eq. (Numerical)
The analytical results are valid only in the “exponential amplification” regime.
In practice, the radiation power “saturates” because of
  Growth of the energy spread
  Decrease of the central energy
The FEL eqs. should be numerically solved to describe the amplification near saturation.

## Slide 34: Results of Simulation

## Slide 35: Example of the Python Code
Main part to solve the 2N+1 equations.
Can be solved easily under 1D and SS condition. Why not try on your own?

## Slide 36
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 37: Classification of FELs
The e- beam moving in the undulator works to “amplify” light
To achieve lasing in FEL, we need
  High gain in total
  Seed light to be amplified
The FELs can be classified according to how to arrange the above condition
Electron Beam
Microbunches
Amplified Light
Undulator
Seed Light
z
x

## Slide 38: Oscillator FELs
Undulator
Oscillator FEL: original concept
Mirror(Optical Cavity)
Amplified many times by different electrons Mode selection by the optical cavity
    single mode laser is possible
    not applicable in shorter-l (x-ray) regions

## Slide 39: Single Pass FELs
Difficulty in oscillator FELs can be overcome by enhancing the gain/pass
  Long undulator
  Higher electron density (lower emittance, higher peak current)
Seed light is amplified by many orders of magnitude even with a single pass
  No cavity is necessary
Further classified into two types according to how to prepare seed light

## Slide 40
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
Characteristics of FEL radiation
  General description of single-pass FELs
ERL: what’s it?

## Slide 41: Important Parameters in SP-FEL(1)
FEL Paramerer r
  Dimensionless parameter related to the efficiency (10-2~10-4)
Gain Length Lg
  Undulator length needed to amplify the radiation power by e=2.718
主要パラメータ

## Slide 42: Important Parameters in SP-FEL(2)
Saturation Power Psat
  Maximum Power Reached in FEL
Saturation Length Lsat
  Undulator length to reach saturation
Conversion efficiency from e- to radiation is r
Number of undulator periods for saturation is r-1
主要パラメータ

## Slide 43: Gain Curve
r
Spont. Rad (SASE)
Exponential Amp.
Saturation

## Slide 44
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
  SASE FEL
ERL: what’s it?

## Slide 45: SASE: Seeded by Spont. Radiation
SASE: Self Amplified Spontaneous Emission
  Spontaneous radiation emitted near the entrance works as the seed light
No special process is needed to prepare seed light
“Shot Noise” dominates the properties of radiation

## Slide 46: Shot Noise
e- distribution contains sparse and dense areas
Radiation profile
temporal
spectral
spatial
angular

## Slide 47: Parameters for Simulation
Electron Beam |  | Undulator | 
Energy | 9 GeV | Period | 20 mm
Bunch Charge | 80 pC | Peak Field | 1.12 T
Bunch Length (FWHM) | 20 fsec | K Value | 2.05
Peak Current | 3.7 kA | Length | 5 m x 10
Norm. Emittance | 0.4 mm | Source Parameter | 
Energy Spread | 10-4 | FEL Parameter | 5.0x10-4
Average Beta | 25 m | Gain Length | 2.1 m
Beam Size (s) | 24 mm | Wavelength | 0.1 nm
Angular Div. (s) | 0.95 mrad | Photon Energy | 12 keV

## Slide 48: Gain Curve
1-m intersection (diagnostics, Q magnets, phase shifters)

## Slide 49: Spectral and Temporal Profiles
物理現象と光特性

## Slide 50: Spiky Structure
sw=rw1
w1
w
sT
t
Fourier
Transform
Time
Domain
Freq.
Domain
sT-1
(rw1)-1
Fourier Limit imposes the widths of envelopes and spikes to be inversely proportional!
物理現象と光特性

## Slide 51: Spatial and Angular Profiles
物理現象と光特性

## Slide 52: Coherence Improvement

## Slide 53
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
  Seeded FEL
ERL: what’s it?

## Slide 54: Seeded Light in FELs
Oscillator FEL: Mode-selected light
  Single mode available
SASE FEL：Shot noise (Spont. Rad.)
  Spatially coherent (optical guiding)
  Temporally partially coherent (poor coherence)
Seeded FEL: Coherent light (seed laser)
  Perfect coherence in time and space (single mode)
  “Coherent-seed” FEL

## Slide 55: How to Realize Short-l Seeded FEL?
HHG
HGHG
Self Seed
High Power Laser
Dispersive
Section
Monochromator
Undulator
Gas Target
Modulator
Radiator
High Power Laser

## Slide 56: Pros and Cons
HHG & HGHG
  External laser needed
  Shorter wavelength using high harmonics
    Interaction with gas (HHG)/
    HHs in microbunches (HGHG)
  Timing (& spatial overlap) is the key issue
  How to go toward shorter l?
Self Seed
  Monochromatized SASE radiation as seed
  No limitations for timing and shorter l
  Seed power fluctuates shot-by-shot

## Slide 57: Parameters for HGHG Simulation
Electron Beam |  | Modulator |  | Radiator | 
Energy | 1.2 GeV | Period | 50 mm | Period | 28 mm
Bunch Charge | 100 pC | Peak Field | 0.72 T | Peak Field | 0.63 T
Bunch Length (FWHM) | 80 fsec | Length | 3.2 m x 2 | Length | 3.2 m x 4
Peak Current | 1.2 kA | K Value | 3.35 | K Value | 1.65
Emittance | 0.4 mm | Seed Parameter |  | Source Parameter | 
Energy Spread | 10-4 | Peak Power | 100 kW | FEL Parameter | 2.0x10-3
Average Beta | 10 m | Wavelength | 30 nm | Gain Length | 0.66 m
Beam Size (s) | 41 mm | Pulse Length | 20 fs | Wavelength | 6 nm
Ang. Div. (s) | 4.1 mrad | Beam Size | 0.35 mm | Photon Energy | 0.2 keV
Modulator
Radiator
30nm
6nm

## Slide 58: Comparison with SASE: Gain Curve
Modulator (HGHG)

## Slide 59: Comparison with SASE: Spectrum

## Slide 60
Introduction
Coherent radiation & FELs
Amplification mechanism in FELs
FEL equation
Characteristics of FEL radiation
ERL: what’s it?

## Slide 61: Low Rep. Rate in NC Linac
Low rep. rate: biggest drawback of FELs based on NC linac
SACLA
Bpeak@SACLA Bpeak@SP8
Bav@SACLA ~ Bav@SP8

## Slide 62: Increasing the Rep. Rate
Rep. rate in NC cavity is limited by the Ohmic loss: pulse operation mandatory (~100 Hz)
  Iav=100pC x 100Hz=10nA (cf. 100mA in storage ring)
SC cavity completely solves the problem; CW operation possible!
  Iav = 100 pC x 1 Gz = 100 mA
However, we have to generate and handle e- beam with huge (average) power
  100mA x 10GeV=1GW (average)
  Nuclear reactor typical power~1GW

## Slide 63: ERL: Energy Recovery Linac
undulator
long undulator or canted undulator
superconducting accelerator
electron gun
beam dump
Electron beam is decelerated by the SC linac in the 2nd turn:
  return its energy to be used to accelerate the next electron beam
  safely discarded

## Slide 64: Application of ERL as a Light Source
EUV-FEL for lithography
  High average power (>kW) light source is strongly desired for EUV litho.
Diffraction-limited synchrotron radiation source (cf. storage ring)
  Much lower emittance enhances the spatial coherence
  Much shorter bunch length may help the time-resolve experiments

## Slide 65: Pros and Cons
 | Storage Ring | NC Linac | ERL
Emittance | △ | ◎ | ◎
Energy Spread | △ | ◎ | ◎
Peak Current | △ | ◎ | 〇
Bunch Length | × | ◎ | ◎
Rep. Rate | ◎ | × | ◎
Stability | ◎ | △ | ?
# Users | ◎ | × | ◎
ERL has many advantages over other competing machines; thus, R&D activities are ongoing toward realization.