## Slide 1
Masao KURIKI
Graduate School of Advanced Sciences of Matter,
Hiroshima University
ALLPPT.com _ Free PowerPoint Templates, Diagrams and Charts
Phase-space rotation technique and applications

## Slide 2: Contents
Introduction
Emittance Exchange
Applications.
Summary

## Slide 3: Introduction
Area of the phase-space occupied by particles: emittance.
In principle, the emittance is the volume in 6D phase-space.
The 6D emittance is invariant (Loisville's theorem).
ｘ
px
z
ｙ
ｘ
px
py
pz

## Slide 4: Louisville's theorem
6D emittance is invariant.
2D emittance (ex, ey, ez) can be conserved, but not invariant.
Can the partitioning of x, y, and z be modified as we want? (Phase-space rotation).
Emittance | ex | ey | ez | ex*ey*ez
No coupling | conserved | convserved | conserved | Invariant
With coupling | varied | varied | varied | Invarian

## Slide 5: XY-Z Emittance Exchange TLEX (Transverse to Longitudinal Emittance eXchange)

## Slide 6: XY-Z Emittance Exchange TLEX
TLEX can be made with chicane or two doglegs and a dipole mode RF cavity.
The phase spaces of X(transverse direction in deflecting plane) and Z (longitudinal direction) are swapped.

## Slide 7: Transfer Matrix
One dog-leg section
One dog-leg section
Dispersion
Momentum compaction
Effective length

## Slide 8: Transfer Matrix of Dipole RF
By/B0
Ez/E0
TM011cavity

## Slide 9: Matrices -EEX section-
matching condition
x-z space exchange
by the 4D space rotation.
compression
factor
dilution
factor
x0
z1
otsuki

## Slide 10: Tunable Subpicosecond Electron-Bunch-Train Generation Using a Transverse-To-Longitudinal Phase-Space Exchange Technique
Y.-E Sun, et al.,
PRL(105)2340801(2010)

## Slide 11
Primary modulation
(slits in x)
After Z-X rotation
(y corresponds to z)
RMS<300fs
(limited by resolution)

## Slide 12
XY Emittance Exchange
RFTB(Round to Flat Beam Transformation)

## Slide 13: Magnetized Beam
Vector Potential
In sigma matrix
Magnetized Beam
Beam Generation in solenoid field (Bz)
Canonical momentum by Vector potential has the angular momentum.
By the fringe field, the canonical momentum becomes the kinetic momentum .
The x-py and y-px correlated beam is obtained.

## Slide 14: Restoration Matrix
E. Thrane, LINAC2002
By ignoring the intrinsic emittance, the beam at the exit of the solenoid field is (x and y are correlated.)
Beam transfer with a matrix M is
If the condition is satisfied, Y1 is independent from X0. The correlation is restored.

## Slide 15: How to restore?
Sigma matrix at the downstream of solenoid field.
M should vanish the non-diagonal component (LJ) of the sigma matrix.

## Slide 16: M matrix
Let us assume three skew Qs
Assume
To satisfy

## Slide 17: Restoration Matrix
E. Thrane, LINAC2002
After skew Q channel,

## Slide 18
P.Piot, Y.-E Sun, K.-J. Kim
PRSTAB(9)031001(2006)
Emittance Ratio 100
was achieved.

## Slide 19: Possible Applications
Emittance exchange is useful to optimize the phase-space distribution to applications.
Examples are
  Pre-bunched FEL,
  Coherent Smith-Parcels radiation,
  Extremely short pulse generation,
  High aspect ratio beam for linear colliders

## Slide 20
Neil Thompson., et al. "The 4GLS VUV-FEL." University of Strathclyde (2011).
High Gain FEL

## Slide 21: Coherent Radiation with Bunch Train
v
Y.-E Sun, et al.,
PRL(105)2340801(2010)

## Slide 22: Asymmetric Beam for Linear Collider
Linear Collider is an only solution for e+e- collision beyond the limit of ring colliders by the huge energy loss by synchrotron radiation.
The beam is “one pass” and the beam current is very limited. In order of 10mA for linear colliders, and in order of A for a modern ring collider .
To obtain an enough luminosity, the beam is focused down to nm.

## Slide 23: High Aspect Ratio Beam in LC
σy«σx
(Asymmetric Beam)
23
Event Rate
Luminosity
Beamstrahlung
Disruption
Parameter | Value
Horizontal size | 640 nm
Vertical size | 5.7 nm
Bunch length | 300 mm
Vertical Disruption | 19.4
RMS energy by BS | 2.4%
Horizontal emi. | 10 mm.mrad
Vertical emi. | 0.04 mm.mrad
Aspect ratio 250 is made
up with 3km DR
Notes: 23

## Slide 24
The high aspect ratio beam is generated by a 3km DR (Damping Ring) in the current design (ILC TDR)..
I the beam can be generated directly from the injector with EmiX technique, the design can be much simpler.
High Aspect Ratio Beam by EMIX

## Slide 25: Flat Beam Generation for LC
The flat beam (ex=10um, ey=0.04um) can be generated with RFTB and TLEX.
The beam is generated in a large size to compensate the space charge non-linearity. ex=ey=45 um.
By RFTB, it can be ex=66000um and ey=0.03.
The ex is too large for LC. It should be exchanged with ez by TLEX.

## Slide 26: High Aspect Ratio Beam Generation with EmiX
GaAs/GaAsP
Super-lattice
laser
Polarized Beam
B field
To booster
Skew Quadrupoles
Injector Linac
Dipole Mode
RF cavity
Dogleg
Dogleg

## Slide 27: STF RF Gun
L-band (1.3 GHz) normal conducting RF gun developed for FLASH/XFEL at DESY.
By switching current of the bucking coil, solenoid field can be made on the cathode surface.
In the simulation, that was 0.1 Tesla.
Cathode Position

## Slide 28: RFTB Section
GaAs/GaAsP
Super-lattice
laser
Polarized Beam
B field
Skew Quadrupoles
Accelerator
The beam is generated in 0.1 Tesla selenoid field.
The canonical angular momentum is converted in the free-space.
The beam is accelerated and the correlation is restored by skew-Q channel.

## Slide 29: Phase-space in RFTB
Before 1st Skew
Before 2nd Skew
Before 3rd Skew
After 3rd Skew

## Slide 30: TLEX Section
ex and ez are exchanged by TLEX beam line.
The large ex after RFTB is transferred to Z space after TLEX.
ex after TLEX section is same as ez before TLEX line.
To booster
Dipole Mode
RF cavity
Dogleg
Dogleg

## Slide 31: Phase-space in TLEX
Before 1st Dogleg
After 1st Dogleg
After dipole RF
After 2nd Dogleg

## Slide 32: Emittance Evolution
ey
ex
ez
Position | ex | ey | ez
Cathode | 1.5 | 1.5 | 8.5
RFTB | 160 | 0.045 | 8.5
TLEX | 8.5 | 0.045 | 160
ILC design | 10 | 0.04 | 8.4e+5
(norm. in um)

## Slide 33: Parameters
Parameter | Value | Unit
Bsol | 0.1 | T
Initial emittance | 1.5 | mm.mrad
Bunch length | 12 | ps (full width)
Beam size | 1.6 | mm (rms)
Gamma after acc. | 49 | 
g1 | -0.503 | T/m
g2 | 0.926 | T/m
g3 | 2.058 | T/m
alpha | 0.3 | rad
η (dispersion) | 0.355 | m
ξ(mom. compaction) | 0.106 | m
RF voltage | 1.29 | MV (at λ)

## Slide 34: Flat Beam Generation at STF and WFA
RFBT experiment will be carried at KEK-STF.
TLEX experiment will be carried out at ANL WFA.
These works will be carried out in 2018 and 2019.
The flat beam compatible to LC will be demonstrated in STF by introducing the TLEX beam line as a future proposal.
RFTB + TLEX section
KEK-STF
ANL-WFA

## Slide 35: Summary
Emittance exchange gives a freedom to optimize the emittance partitioning among degree of freedom.
Applications : High gain FEL, coherent radiation, extremely short bunch generation, flat beam for LC, etc.
ILC compatible beam can be made with these techniques.
Pilot experiments will be carried out at KEK-STF and ANL-WFA.
It can be a proposal for a future plan of STF.

## Slide 36: Acknowledgement
P. Piot (Northrn Illinois University)
J. Power (ANL)
H. Hayano, N. Yamamoto, Y. Seimiya (KEK)
S. Kashiwagi (Tohoku University)
K. Sakaue, M. Wahio (Waseda University)
This work is partly supported by Japan-US
cooperativegrant for scientific studies,
Grant aid for scientific study by MEXT Japan (KAKENHI)